## Slide 1: Computer Graphics
Bing-Yu Chen National Taiwan University

## Slide 2: Introduction
The Graphics Process
Color Models
Triangle Meshes
The Rendering Pipeline

## Slide 3: What is Computer Graphics ?
Definition
  the pictorial synthesis of real or imaginary objects from their computer-based models
 | descriptions | images
descriptions |  | Computer Graphics
images | Computer Vision Pattern Recognition | Image Processing
OUTPUT
INPUT

## Slide 4: What is Computer Graphics ?
modeling
rendering
animation
Notes: More academic. Today is the most related to industry.
I am not an expert, it is just my understaning to vfx

## Slide 5: Applications
Movies
Interactive entertainment
Industrial design
Architecture
Culture heritage

## Slide 6: The Graphics Process
Lighting
Information
Texture
Information
Rendering
Image Storage & Display
3D Geometric Models
3D Animation Definition

## Slide 7: Basic Graphics System
Input devices
Output device
Image formed in FB

## Slide 8: Synthetic Camera Model
camera
image plane/view plane
projector
p
projection of p
objects/models
view frustrum/view volume
lighting

## Slide 9: Elements of Image Formation
Objects
Viewer
Light source(s)
Attributes that govern how light interacts with the materials in the scene
Note the independence of the objects, viewer, and light source(s)

## Slide 10: Light
Light is the part of the electromagnetic spectrum that causes a reaction in our visual systems
Generally these are wavelengths in the range of about 350-750 nm (nanometers)
Long wavelengths appear as reds and short wavelengths as blues

## Slide 11: Luminance and Color Images
Luminance
  Monochromatic
  Values are gray levels
  Analogous to working with black and white film or television
Color
  Has perceptional attributes of hue, saturation, and lightness
  Do we have to match every frequency in visible spectrum? No!

## Slide 12: Three-Color Theory
Human visual system has two types of sensors
  Rods: monochromatic, night vision
  Cones
    Color sensitive
    Three types of cone
    Only three values (the tristimulus
    values) are sent to the brain
Need only match these three values
  Need only three primary colors

## Slide 13: Additive and Subtractive Color
Additive color
  Form a color by adding amounts of three primaries
    CRTs, projection systems, positive film
  Primaries are Red (R), Green (G), Blue (B)
Subtractive color
  Form a color by filtering white light with Cyan (C), Magenta (M), and Yellow (Y) filters
    Light-material interactions
    Printing
    Negative film

## Slide 14: The RGB Color Model – for CRT
Black=(0,0,0)
Red=(1,0,0)
Green=(0,1,0)
White=(1,1,1)
Yellow=(1,1,0)
Cyan=(0,1,1)
Blue=(0,0,1)
Magenta=(1,0,1)

## Slide 15: Color Depth
Can choose number of bits for each of r, g and b
  More bits per component means more colors can be distinguished, but image files will be larger
  8 bits (1 byte) per component: 24-bit color, millions of colors
If r = g = b, color is a shade of gray, so grayscale can be represented by a single value
  8 bits permits 256 grays

## Slide 16: The CMY Color Model – for hardcopy
Black=(0,0,0)
Red=(1,0,0)
Yellow=(1,1,0)
Magenta=(1,0,1)
Blue=(0,0,1)
Cyan=(0,1,1)
Green=(0,1,0)
White=(1,1,1)

## Slide 17: Undercolor Removal: CMYK System
Real inks do not correspond to ideal subtractive primaries
Combining three inks for black is undesirable
Printers use four process colors, cyan, magenta, yellow and black
CMYK gamut is not the same as RGB
  Implications for using images prepared for print (CMYK) on the Web (RGB)

## Slide 18: The CMYK Color Model – for hardcopy
    C = G+B = W-R
    M = R+B = W-G
    Y = R+G = W-B
    K = min(C,M,Y)
    C C-K
    M M-K
    Y Y-K

## Slide 19: The HSV Color Model – for user-oriented
Alternative way of specifying color
Hue (roughly, dominant wavelength)
Saturation (purity)
Value (brightness)
Model HSV as a cylinder: H angle, S distance from axis, V distance along axis
Basis of popular style of color picker

## Slide 20: The HSV Color Model – for user-oriented
H : hue
S : saturation
V : value
  (or B for blight)
Magenta
Black
Red
Green
White
Yellow
Cyan
Blue
H
S
V
0.0
1.0
0°
120°
240°

## Slide 21: Color Models in Video
Largely derive from older analog methods of coding color for TV. Luminance is separated from color information.
YIQ is used to transmit TV signals in North America and Japan. This coding also makes its way into VHS video tape coding in these countries since video tape technologies also use YIQ.
In Europe, video tape uses the PAL or SECAM codings, which are based on TV that uses a matrix transform called YUV.
Digital video mostly uses a matrix transform called YCbCr that is closely related to YUV.

## Slide 22: The YUV Color Model – for PAL video
Can be useful to separate brightness and color information, especially for video.
Y is for luminance and U and V are for chrominance which are stored as two color difference values B-Y and R-Y.

## Slide 23: The YUV Color Model – for PAL video
For dealing with composite video, it turns out to be convenient to contain U and V within the range −1/3 to +4/3. So U and V are rescaled:
The chrominance signal = the composite signal C:

## Slide 24: The YIQ Color Model – for NTSC color-TV
Y : luminance
I and Q : chromaticity (rotated version of U and V)

## Slide 25: The YCbCr Color Model – for digital video
scaled to [0-255]

## Slide 26: Pinhole Camera
Use trigonometry to find projection of a point
These are equations of simple perspective
xp= -x/z/d
yp= -y/z/d
zp= d

## Slide 27: Basics of Rendering
Pipeline Based Rendering
  Objects in the scene are rendered in a sequence of steps that form the Rendering Pipeline.
Ray-Tracing
  A series of rays are projected thru the view plane and the view plane is colored based on the object that the ray strikes

## Slide 28: Ray Tracing and Geometric Optics
One way to form an image is to follow rays of light from a point source determine which rays enter the lens of the camera. However, each ray of light may have multiple interactions with objects before being absorbed or going to infinity.

## Slide 29: Global vs. Local Lighting
Cannot compute color or shade of each object independently
  Some objects are blocked from light
  Light can reflect from object to object
  Some objects might be translucent

## Slide 30: Why not ray tracing?
Ray tracing seems more physically based so why don’t we use it to design a graphics system?
Possible and is actually simple for simple objects such as polygons and quadrics with simple point sources
In principle, can produce global lighting effects such as shadows and multiple reflections but is slow and not well-suited for interactive applications

## Slide 31: Pipeline Rendering
Transform
Illuminate
Transform
Clip
Project
Rasterize
Model & Camera Parameters
Rendering Pipeline
Framebuffer
Display

## Slide 32: Architecture of a Raster Display
Video controller
Display controller (DC)
Interface with host computer
(Display commands)
(Interaction data)
Refresh buffer
Keyboard
Mouse
0000000000000000000000000
0000000000000000000111000
0000000000000000011100000
0000000000000000001100000
0000000000000000000011000
0000000000001110000000000
0000000011111111111000000
0001111111111111111111110
0001111111000000011111110
0001111111111111111111110
0001111111000000011111110
0001111111000000011111110
0001111111000000011111110
0001111111000000011111110
0001111111111111111111110
0000000000000000000000000

## Slide 33: Definitions of Triangle Meshes
{f1} : { v1 , v2 , v3 } {f2} : { v3 , v2 , v4 } …
connectivity
geometry
{v1} : (x,y,z) {v2} : (x,y,z) …
face attributes
{f1} : “skin material” {f2} : “brown hair” …
[Hoppe 99’]
Notes: In computer graphics, geometric models are commonly represented as triangle meshes.
As shown here, a mesh consists of a set of triangular faces pasted together along their edges and meeting at a common set of vertices.
In a traditional representation, a mesh is represented as a set of vertices containing xyz coordinates, and a set of faces containing indices referring back to the vertices.
Besides geometry, other appearance attributes are often present in a mesh, such as vertex normals, vertex colors, material attributes, and texture maps. These appearance attributes are also associated with the vertices and faces of the mesh.

## Slide 34: Definitions of Triangle Meshes
{v2,f1} : (nx,ny,nz) (u,v) {v2,f2} : (nx,ny,nz) (u,v) …
corner attributes
{f1} : { v1 , v2 , v3 } {f2} : { v3 , v2 , v4 } …
connectivity
geometry
{v1} : (x,y,z) {v2} : (x,y,z) …
face attributes
{f1} : “skin material” {f2} : “brown hair” …
[Hoppe 99’]

## Slide 35: Definitions of Triangle Meshes
face
edge
different material properties
(face attributes)
different normal vectors
(corner attributes)
vertex
boundary
wedge
corner
Notes: A geometric 3D model is usually represented as triangular meshes. If either an edge is a boundary edge, or its adjacent vertices have different normal vectors, or its two adjacent faces have different material properties, this edge is called a sharp edge, like the blue lines in this figure.
３次元モデルは通常三角形メッシュにより表現されています。[ENTER]もし、あるエッジが境界エッジであるか、[ENTER]このエッジに隣接する２つの頂点が異なる法線ベクトルをもつか、あるいは[ENTER]このエッジに隣接する２つの面が異なる材質属性をもつならば、[ENTER]そのエッジはシャープエッジと定義します。例えば、画面上の青い線です。[ENTER]

## Slide 36: Rendering: Transformations
So far, discussion has been in screen space
But model is stored in model space (a.k.a. object space or world space)
Three sets of geometric transformations:
  Modeling transforms
  Viewing transforms
  Projection transforms

## Slide 37: The Rendering Pipeline
Scene graph Object geometry
Lighting Calculations
Clipping
Modeling Transforms
Viewing Transform
Projection Transform
Rasterization

## Slide 38: Rendering Pipeline for z-buffer & Gouraud shading
Viewing transformation
db traversal
Modeling transformation
Trivial accept / reject
Lighting
Clipping
Divide by W, map to 3D viewport
Rasterization
Display

## Slide 39: APPENDIX:
History of Computer Graphics

## Slide 40: Computer Graphics: 1950-1960
Computer graphics goes back to the earliest days of computing
  Strip charts
  Pen plotters
  Simple displays using A/D converters to go from computer to calligraphic CRT
Cost of refresh for CRT too high
  Computers slow, expensive, unreliable

## Slide 41: Computer Graphics: 1960-1970
Wireframe graphics
Project Sketchpad
Display Processors
Storage tube

## Slide 42: Project Sketchpad
Ivan Sutherland’s PhD thesis at MIT
  Recognized the potential of man-machine interaction
  Loop
    Display something
    User moves light pen
    Computer generates new display
  Sutherland also created many of the now common algorithms for computer graphics

## Slide 43: Display Processor
Rather than have host computer try to refresh display use a special purpose computer called a display processor (DPU)
Graphics stored in display list (display file) on display processor
Host compiles display list and sends to DPU

## Slide 44: Direct View Storage Tube
Created by Tektronix
  Did not require constant refresh
  Standard interface to computers
    Allowed for standard software
    Plot3D in Fortran
  Relatively inexpensive
    Opened door to use of computer graphics for CAD community

## Slide 45: Computer Graphics: 1970-1980
Raster Graphics
Beginning of graphics standards
  IFIPS
    GKS: European effort
      Becomes ISO 2D standard
    Core: North American effort
      3D but fails to become ISO standard
Workstations and PCs

## Slide 46: Raster Graphics
Image produced as an array (the raster) of picture elements (pixels) in the frame buffer

## Slide 47: Raster Graphics
Allow us to go from lines and wireframes to filled polygons

## Slide 48: PCs and Workstations
Although we no longer make the distinction between workstations and PCs historically they evolved from different roots
  Early workstations characterized by
    Networked connection: client-server
    High-level of interactivity
  Early PCs included frame buffer as part of user memory

## Slide 49: Computer Graphics: 1980-1990
Realism comes to computer graphics
smooth shading
environmental
mapping
bump mapping

## Slide 50: Computer Graphics: 1980-1990
Special purpose hardware
  Silicon Graphics geometry engine
    VLSI implementation of graphics pipline
Industry-based standards
  PHIGS
  RenderMan
Networked graphics: X Window System
Human-Computer Interface (HCI)

## Slide 51: Computer Graphics: 1990-2000
OpenGL API
Completely computer-generated feature-length movies (Toy Story) are successful
New hardware capabilities
  Texture mapping
  Blending
  Accumulation, stencil buffer

## Slide 52: Computer Graphics: 2000-
Photorealism
Graphics cards for PCs dominate market
  Nvidia, ATI, 3DLabs
Game boxes and game players determine direction of market
Computer graphics routine in movie industry: Maya, Lightwave