## Slide 1: Computer Graphics
Bing-Yu Chen National Taiwan University

## Slide 2: Viewing in 3D
3D Viewing Process
Classical Viewing and Projections
3D Synthetic Camera Model
Parallel Projection
Perspective Projection
3D Clipping for Canonical View Volume

## Slide 3: 3D Viewing Process
Transform into viewport in 2D device coordinates for display
Project onto projection plane
Clip against view volume
2D device coordinates
Clipped world coordinates
3D world-coordinate output primitives

## Slide 4: Classical Viewing
Viewing requires three basic elements
  One or more objects
  A viewer with a projection surface
  Projectors that go from the object(s) to the projection surface
Classical views are based on the relationship among these elements
  The viewer picks up the object and orients it how she would like to see it
Each object is assumed to constructed from flat principal faces
  Buildings, polyhedra, manufactured objects

## Slide 5: Planar Geometric Projections
Standard projections project onto a plane
Projectors are lines that either
  converge at a center of projection are parallel
Such projections preserve lines
  but not necessarily angles
Nonplanar projections are needed for applications such as map construction

## Slide 6: Classical Projections
Front elevation
Elevation oblique
Plan oblique
Isometric
One-point perspective
Three-point perspective

## Slide 7: 3D Synthetic Camera Model
The synthetic camera model involves two components, specified independently:
  objects (a.k.a geometry)
  viewer (a.k.a camera)

## Slide 8: Imaging with the Synthetic Camera
center of projection
image plane
projector
P
projection of P
The image is rendered onto an image plane or project plane (usually in front of the camera).
Projectors emanate from the center of projection (COP) at the center of the lens (or pinhole).
The image of an object point P is at the intersection of the projector through P and the image plane.

## Slide 9: Specifying a Viewer
Camera specification requires four kinds of parameters:
  Position: the COP.
  Orientation: rotations about axes with origin at the COP.
  Focal length: determines the size of the image on the film plane, or the field of view.
  Film plane: its width and height, and possibly orientation.

## Slide 10: Projections
Projections transform points in n-space to m-space, where m < n.
In 3D, we map points from 3-space to the projection plane (PP) along projectors emanating from the center of projection (COP).
There are two basic type of projections:
  Perspective – distance from COP to PP finite
  Parallel – distance from COP to PP infinite
COP
PP

## Slide 11: Perspective vs. Parallel Projections
Computer graphics treats all projections the same and implements them with a single pipeline
Classical viewing developed different techniques for drawing each type of projection
Fundamental distinction is between parallel and perspective viewing even though mathematically parallel viewing is the limit of perspective viewing

## Slide 12: Perspective vs. Parallel Projections

## Slide 13: Taxonomy of Planar Geometric Projections
parallel
perspective
axonometric
multiview
orthographic
oblique
isometric
dimetric
trimetric
2 point
1 point
3 point
planar geometric projections

## Slide 14: Orthographic Projection
Projectors are orthogonal to projection surface

## Slide 15: Multiview Orthographic Projection
Projection plane parallel to principal face
Usually form front, top, side views
isometric (not multiview
orthographic view)
front
side
top
in CAD and architecture,
we often display three
multiviews plus isometric

## Slide 16: Advantages and Disadvantages
Preserves both distances and angles
  Shapes preserved
  Can be used for measurements
    Building plans
    Manuals
Cannot see what object really looks like because many surfaces hidden from view
  Often we add the isometric

## Slide 17: Axonometric Projections
classify by how many angles of
a corner of a projected cube are
the same
none: trimetric
two: dimetric
three: isometric
q 1
q 3
q 2
Allow projection plane to move relative to object

## Slide 18: Types of Axonometric Projections
Isometric
Trimetric
Dimetric

## Slide 19: Advantages and Disadvantages
Lines are scaled (foreshortened) but can find scaling factors
Lines preserved but angles are not
  Projection of a circle in a plane not parallel to the projection plane is an ellipse
Can see three principal faces of a box-like object
Some optical illusions possible
  Parallel lines appear to diverge
Does not look real because far objects are scaled the same as near objects
Used in CAD applications

## Slide 20: Oblique Projection
Arbitrary relationship between projectors and projection plane

## Slide 21: Advantages and Disadvantages
Can pick the angles to emphasize a particular face
  Architecture: plan oblique, elevation oblique
Angles in faces parallel to projection plane are preserved while we can still see “around” side
In physical world, cannot create with simple camera; possible with bellows camera or special lens (architectural)

## Slide 22: Specification of an Arbitrary 3D View
VRP: view reference point
VPN: view-plane normal
VUP: view-up vector
n
u
VUP
VPN
VRP
v
View plane

## Slide 23: VRC: the viewing-reference coordinate system
CW: center of the window
n
u
VPN
VRP
v
CW
View plane
(umax,vmax)
(umin,vmin)

## Slide 24: Infinite Parallelepiped View Volume
DOP: direction of projection
PRP: projection reference point
PRP
DOP
CW
View plane
n
VPN
VRP

## Slide 25: Truncated View Volume for an Orthographic Parallel Projection
DOP
VPN
VRP
View
plane
Front
Clipping
plane
Back
Clipping
plane
F
B

## Slide 26: The Mathematics of Orthographic Parallel Projection
y
x
z
z
P(x, y, z)
P(x, y, z)
yp
xp
View along x axis
View along y axis
Projection
plane
Projection
plane

## Slide 27: The Steps of Implementation of Orthographic Parallel Projection
Translate the VRP to the origin
Rotate VRC such that the VPN becomes the z axis
Shear such that the DOP becomes parallel to the z axis
Translate and scale into the parallel-projection canonical view volume

## Slide 28: Perspective Projection
Projectors converge at center of projection

## Slide 29: Truncated View Volume for an Perspective Projection
VPN
VRP
View
plane
Front
Clipping
plane
Back
Clipping
plane
F
B

## Slide 30: Perspective Projection (Pinhole Camera)
y
x
z
z
P(x, y, z)
P(x, y, z)
d
d
yp
xp
View along x axis
View along y axis
Projection
plane
Projection
plane

## Slide 31: Perspective Division
However W  1, so we must divide by W to return from homogeneous coordinates

## Slide 32: The Steps of Implementation of Perspective Projection
Translate the VRP to the origin
Rotate VRC such that the VPN becomes the z axis
Translate such that the PRP is at the origin
Shear such that the DOP becomes parallel to the z axis
Scale such that the view volume becomes the canonical perspective view volume

## Slide 33: Alternative Perspective Projection
y
z
z
P(x, y, z)
P(x, y, z)
d
d
yp
xp
View along x axis
View along y axis
Projection
plane at z=0
Projection
plane at z=0

## Slide 34: Vanishing Points
Parallel lines (not parallel to the projection plan) on the object converge at a single point in the projection (the vanishing point)
Drawing simple perspectives by hand uses these vanishing point(s)
vanishing point

## Slide 35: Three-Point Perspective
No principal face parallel to projection plane
Three vanishing points for cube

## Slide 36: Two-Point Perspective
On principal direction parallel to projection plane
Two vanishing points for cube

## Slide 37: One-Point Perspective
One principal face parallel to projection plane
One vanishing point for cube

## Slide 38: Advantages and Disadvantages
Objects further from viewer are projected smaller than the same sized objects closer to the viewer (diminuition)
  Looks realistic
Equal distances along a line are not projected into equal distances (nonuniform foreshortening)
Angles preserved only in planes parallel to the projection plane
More difficult to construct by hand than parallel projections (but not more difficult by computer)

## Slide 39: Canonical View Volume for Orthographic Parallel Projection
x = -1, y = -1, z = 0
x = 1, y = 1, z = -1
-1
-1
1
-z
x or y
Back
plane
Front
plane

## Slide 40: The Extension of the Cohen-Sutherland Algorithm
bit 1 – point is above view volume y > 1
bit 2 – point is below view volume y < -1
bit 3 – point is right of view volume x > 1
bit 4 – point is left of view volume x < -1
bit 5 – point is behind view volume z < -1
bit 6 – point is in front of view volume z > 0

## Slide 41: Intersection of a 3D Line
a line from to can be represented as
so when y = 1

## Slide 42: Canonical View Volume for Perspective Projection
x = z, y = z, z = -zmin
x = -z, y = -z, z = -1
-1
-1
1
-z
x or y
Back
plane
Front
plane

## Slide 43: The Extension of the Cohen-Sutherland Algorithm
bit 1 – point is above view volume y > -z
bit 2 – point is below view volume y < z
bit 3 – point is right of view volume x > -z
bit 4 – point is left of view volume x < z
bit 5 – point is behind view volume z < -1
bit 6 – point is in front of view volume z > zmin

## Slide 44: Intersection of a 3D Line
so when y = z

## Slide 45: Clipping in Homogeneous Coordinates
Why clip in homogeneous coordinates ?
  it is possible to transform the perspective-projection canonical view volume into the parallel-projection canonical view volume

## Slide 46: Clipping in Homogeneous Coordinates
The corresponding plane equations are
  X = -W
  X = W
  Y = -W
  Y = W
  Z = -W
  Z = 0