## Slide 1: Computer Graphics
Ken-Yi Lee National Taiwan University

## Slide 2: GPGPU and OpenCL
Introduction to GPGPU
  Graphics Pipeline
  GPGPU Programming
Introduction to OpenCL
  OpenCL Framework
  OpenCL C Language
  Example: Dense Matrix Multiplication

## Slide 3: Fixed Functionality Pipeline
Vertices
Frame Buffer
Triangles/Lines/Points
Texture
Environment
Color
Sum
Transform
and
Lighting
Rasterizer
Primitive
Assembly
Depth
Stencil
Alpha
Test
Fog
Dither
Color
Buffer
Blend
API
Vertex
Buffer
Objects
Primitive
Processing
Notes: The slides are from http://people.freedesktop.org/~idr/GLSL_presentation/GLSL-Portland-Benj.PPT

## Slide 4: Programmable Shader Pipeline
Vertices
Frame Buffer
Triangles/Lines/Points
API
Vertex
Shader
Rasterizer
Primitive
Assembly
Fragment
Shader
Depth
Stencil
Color
Buffer
Blend
Vertex
Buffer
Objects
Primitive
Processing
Alpha
Test
Dither

## Slide 5: Programming Model
Vertex
Shader
Fragment
Shader
Primitive
Assembly
& Rasterize
Per-Sample
Operations
Attributes
(m * vec4)
Varyings
(n * vec4)
Uniforms
Textures

## Slide 6: Give Me More Power
Vertex
Shader
Fragment
Shader
Primitive
Assembly
& Rasterize
Per-Sample
Operations
Attributes
(m * vec4)
Varyings
(n * vec4)
Uniforms
Textures
Vertex
Shader
Vertex
Shader
Fragment
Shader
Fragment
Shader

## Slide 7: Introduction to GPGPU
GPGPU: General-Purpose Graphics Processing Unit
  There is a GPU, don’t let it idle ! (better than none)
  Will a program run faster with GPU than CPU ?
    It depends. But note that we used to write programs for CPUs, not GPUs.
    If you care about scalability…

## Slide 8: GPGPU with GLSL: Matrix Addition
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
9 | 7 | 9
0 | 7 | 8
3 | 6 | 8
10 | 9 | 12
4 | 12 | 14
10 | 14 | 17
+
=
Vertex
Shader
Fragment
Shader
Primitive
Assembly
& Rasterize
Per-Sample
Operations
Attributes
Varyings
Uniforms
Textures
Texture0
Texture1
screen
1. Draw a 3x3 rectangle!
2. Calculate in Fragment Shader
3. Output to ?
Frame Buffer

## Slide 9: Render to Texture (FBO)
1
CPU
GPU
Setup
glDraw*()
Vertex Shader 1
Fragment Shader 1
glReadPixels()
Write to FB
glReadPixels()
Setup
glDraw*()
Vertex Shader 2
Fragment Shader 2
Write to FB
CPU
GPU
Setup
glDraw*()
Vertex Shader 1
Fragment Shader 1
Write to FBO
glReadPixels()
Setup
glDraw*()
Vertex Shader 2
Fragment Shader 2
Write to FBO

## Slide 10: Modern GPU Architecture
Unified Shader
INPUT
OUTPUT
Textures
Buffers
Unified Shader Model (Shader Model 4.0)
Stage: VERTEX, FRAGMENT

## Slide 11: A Real Case: GeForce 8800
L2
FB
SP
SP
L1
TF
Vtx Thread Issue
Setup / Rstr / ZCull
Geom Thread Issue
Pixel Thread Issue
Data Assembler
Host
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
L2
FB
L2
FB
L2
FB
L2
FB
L2
FB
Thread Processor
SP
TF
TPC
16 SM 128 SP
SM

## Slide 12: A Real Case: Explained
SP
SP
L1
TF
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Shared Memory
SM
Register File
To hide memory latency

## Slide 13: Modern GPGPU
Get rid of the graphics stuffs !
  I am not a graphics expert but I want to utilize the GPU power !
Beyond graphics !
  NVIDIA CUDA / AMD Stream SDK
  OpenCL
However, you can’t really get rid of it.
  Based on the same device

## Slide 14: Introduction to OpenCL
OpenCL lets Programmers write a single portable program that uses ALL resources in the heterogeneous platform
From http://www.khronos.org/developers/library/overview/opencl_overview.pdf

## Slide 15: How to Use OpenCL ?
To use OpenCL, you must
  Define the platform
  Execute code on the platform
  Move data around in memory
  Write (and build) programs

## Slide 16: Platform Model
Define the platform:
The OpenCL Specification 1.1 (Figure 3.1)
Host (CPU)
Compute Device (8800)
Compute Unit (SM)
Processing Element (SP)
Ex. NVIDIA GeForce 8800

## Slide 17: Execute a Kernel at Each Point
void vec_add( int n, const float *a, const float *b, float *c) {
for (int i=0; i<n; ++i){
c[i] = a[i] + b[i];
}
}
kernel void vec_add ( global const float *a, global const float *b, global float *c) {
int i = get_global_id(0);
c[i] = a[i] + b[i];
}
With a CPU
With a Processing Element
Execute over “n” work-items
The number of Processing Elements is device-dependent. The number of Work Items is problem-dependent.

## Slide 18: Execution Model
Execute code on the platform:
The OpenCL Specification 1.1 (Figure 3.2)
NDRange
Work-Group (CU)
Work-Item (PE)

## Slide 19: Memory Model
Move data around in memory
Memory management is Explicit
Host (Host)
Global / Constant (CD)
Local (CU)
Private (PE)

## Slide 20: Programming Kernels: OpenCL C Language
A subset of ISO C99
  But without some C99 features such as standard C99 headers, function pointers, recursion, variable length arrays, and bit fields
A superset of ISO C99
  Work-items and workgroups
  Vector types
  Synchronization
  Address space qualifier
Also include a large set of built-in functions

## Slide 21: An Example: Vector Addition
__kernel void VectorAdd(
__global const float* a,
__global const float* b,
__global float* c,
int iNumElements)
{
// Get index into global data array
int iGID = get_global_id(0);
// Bound check (equivalent to the limit on a 'for' loop
// for standard/serial C code
if (iGID >= iNumElements)
return;
// Add the vector elements
c[iGID] = a[iGID] + b[iGID];
}
get_global_id(dim_idx)

## Slide 22: Programming Kernels: Data Types
Scalar data types
  char, int, long, float, uchar, …
  bool, size_t, void, …
Image types
  image2d_t, image3d_t, sampler_t
Vector data types
  Vector lengths: 2, 4, 8 & 16
  char2, short4, int8, float16, …

## Slide 23: Memory Objects
Memory objects are categorized into two types:
  Buffer object:
    Stores a one-dimensional collection of elements
    Sequential (directly accessing, pointer)
  Image object:
    Store two- or three- dimensional texture, frame-buffer or image (?)
    Texture (indirectly accessing, built-in function)

## Slide 24: Programming Flow (1)
Creating a context with a command queue:
  clGetPlatformIDs()
  clGetDeviceIDs()
  clCreateContext()
  clCreateCommandQueue()
Device
Memory Objects
Command Queue
Context
Notes: Illustration of Context

## Slide 25: Programming Flow (2)
Memory Allocation & Copying
  clCreateBuffer()
  clEnqueueWriteBuffer()
    Asynchronous
Program Building
  clCreateProgramWithSource()
  clBuildProgram()
Kernel Setting
  clCreateKernel()
  clSetKernelArg()
Kernel
Kernel
Program
Global
Host
Device
Host

## Slide 26: Programming Flow (3)
Kernel Execution:
  clEnqueueNDRangeKernel()
Readback:
  clEnqueueReadBuffer()

## Slide 27: NVIDIA OpenCL Samples
Download webpage:
  http://developer.download.nvidia.com/compute/cuda/3_0/sdk/website/OpenCL/website/samples.html
Used Examples:
  OpenCL Device Query
  OpenCL Vector Addition
  OpenCL Matrix Multiplication
here

## Slide 28: OpenCL Device Query
You can use this program to check your device ability for OpenCL
OpenCL SW Info:
CL_PLATFORM_NAME: NVIDIA CUDA
CL_PLATFORM_VERSION: OpenCL 1.0 CUDA 3.1.1
OpenCL SDK Revision: 7027912
OpenCL Device Info:
1 devices found supporting OpenCL:
---------------------------------
Device GeForce GTS 360M
---------------------------------
CL_DEVICE_NAME: GeForce GTS 360M
CL_DEVICE_VENDOR: NVIDIA Corporation
…

## Slide 29: OpenCL Vector Addition
__kernel void VectorAdd(
__global const float* a,
__global const float* b,
__global float* c,
int iNumElements)
{
// Get index into global data array
int iGID = get_global_id(0);
// Bound check (equivalent to the limit on a 'for' loop
// for standard/serial C code
if (iGID >= iNumElements)
return;
// Add the vector elements
c[iGID] = a[iGID] + b[iGID];
}
Performance ?

## Slide 30: Matrix Multiplication: Simple Version
__kernel void
matrixMul(
__global float* C,
__global float* A,
__global float* B,
int width_A, int width_B)
{
int row = get_global_id(1);
int col = get_global_id(0);
float Csub = 0.0f;
for (int k = 0; k < width_A; ++k) {
Csub += A[row*width_A + k] * B[k*width_B+col];
}
C[row*width_B+ col] = Csub;
}
A
B
C

## Slide 31: Matrix Multiplication: Local Memory (1)
A
B
C
Move a block from A
Move a block from B
Calculate block * block
If no finished, goto Step 1.
Memory Access

## Slide 32: Matrix Multiplication: Local Memory (2)
__kernel void
matrixMul(
__global float* C, __global float* A, __global float* B, __local float* As, __local float* Bs, int width_A, int width_B) {
int Cx = get_group_id(0);
int Cy = get_group_id(1);
int cx = get_local_id(0);
int cy = get_local_id(1);
int Abegin = width_A * BLOCK_SIZE * Cy;
int Aend = Abegin + width_A - 1;
int Astep = BLOCK_SIZE;
int Bbegin = BLOCK_SIZE * Cx;
int Bstep = BLOCK_SIZE * width_B;

## Slide 33: Matrix Multiplication: Local Memory (3)
float Csub = 0.0f;
for (int a = Abegin, b = Bbegin;
a <= Aend;
a += Astep, b += Bstep) {
AS(cy, cx) = A[a + width_A * cy + cx];
BS(cy, cx) = B[b + width_B * cy + cx];
#pragma unroll
for (int k = 0; k < BLOCK_SIZE; ++k)
Csub += AS(cy, k) * BS(k, cx);
}
C[get_global_id(1)*get_global_size(0)+get_global_id(0)] = Csub;
}
Process a block each time
Move
Compute

## Slide 34: OpenCL Synchronization
There are two methods to synchronize between different work-items:
  Local synchronization
    Within the same work-group
    Barrier
  Global synchronization
    Between different work-group / devices
    Event

## Slide 35: Matrix Multiplication: Local Memory (4)
float Csub = 0.0f;
for (int a = Abegin, b = Bbegin;
a <= Aend;
a += Astep, b += Bstep) {
AS(cy, cx) = A[a + width_A * cy + cx];
BS(cy, cx) = B[b + width_B * cy + cx];
barrier(CLK_LOCAL_MEM_FENCE);
#pragma unroll
for (int k = 0; k < BLOCK_SIZE; ++k)
Csub += AS(cy, k) * BS(k, cx);
barrier(CLK_LOCAL_MEM_FENCE);
}
C[get_global_id(1)*get_global_size(0)+get_global_id(0)] = Csub;
}